## Slide 1: TE2023 Microcontrollers Computer Architectures and Instructions
Luis Alfonso Maeda Núñez, PhD
Professor

## Slide 2: Instruction types
Register-to-register
  Format: OPC RS1, RS2, RD
  Behavior: Reg[RS1] (OPC) Reg[RS2] -> Reg[RD]
Immediate type
  Format: OPC RS, RD, Immediate
  Behavior: Reg[RS] (OPC) Immediate -> Reg[RD]
Jump type
  Format: OPC Immediate
  Behavior: Immediate -> PC

## Slide 3: CPU Architecture

## Slide 4: ALU Register-Register Instructions
Encoding |  |  |  |  |  | OPC | Op1 | Op2 | Op3 | Operation
0 | 0 | 0 | 0 | 0 | 0 | ADD | RS1 | RS2 | RD | Reg[RS1] + Reg[RS2] -> Reg[RD]
0 | 0 | 0 | 0 | 0 | 1 | SUB | RS1 | RS2 | RD | Reg[RS1] - Reg[RS2] -> Reg[RD]
0 | 0 | 0 | 0 | 1 | 0 | AND | RS1 | RS2 | RD | Reg[RS1] & Reg[RS2] -> Reg[RD]
0 | 0 | 0 | 0 | 1 | 1 | OR | RS1 | RS2 | RD | Reg[RS1] ¦ Reg[RS2] -> Reg[RD]
0 | 0 | 0 | 1 | 0 | 0 | XOR | RS1 | RS2 | RD | Reg[RS1] ^ Reg[RS2] -> Reg[RD]
0 | 0 | 0 | 1 | 0 | 1 | NAND | RS1 | RS2 | RD | ~(Reg[RS1] & Reg[RS2]) -> Reg[RD]
0 | 0 | 0 | 1 | 1 | 0 | NOR | RS1 | RS2 | RD | ~(Reg[RS1] ¦ Reg[RS2]) -> Reg[RD]
0 | 0 | 0 | 1 | 1 | 1 | XNOR | RS1 | RS2 | RD | ~(Reg[RS1] ^ Reg[RS2]) -> Reg[RD]
0 | 0 | 1 | 0 | 0 | 0 | SL | RS1 | RS2 | RD | Reg[RS1] << Reg[RS2] -> Reg[RD]
0 | 0 | 1 | 0 | 0 | 1 | SR | RS1 | RS2 | RD | Reg[RS1] >> Reg[RS2] -> Reg[RD]
0 | 0 | 1 | 0 | 1 | 0 | SGE | RS1 | RS2 | RD | If Reg[RS1] >= Reg[RS2] then 1 -> Reg[RD] else 0 -> Reg[RD]
0 | 0 | 1 | 0 | 1 | 1 | SGT | RS1 | RS2 | RD | If Reg[RS1] > Reg[RS2] then 1 -> Reg[RD] else 0 -> Reg[RD]
0 | 0 | 1 | 1 | 0 | 0 | SLE | RS1 | RS2 | RD | If Reg[RS1] <= Reg[RS2] then 1 -> Reg[RD] else 0 -> Reg[RD]
0 | 0 | 1 | 1 | 0 | 1 | SLT | RS1 | RS2 | RD | If Reg[RS1] < Reg[RS2] then 1 -> Reg[RD] else 0 -> Reg[RD]
0 | 0 | 1 | 1 | 1 | 0 | SEQ | RS1 | RS2 | RD | If Reg[RS1] == Reg[RS2] then 1 -> Reg[RD] else 0 -> Reg[RD]
0 | 0 | 1 | 1 | 1 | 1 | SNE | RS1 | RS2 | RD | If Reg[RS1] != Reg[RS2] then 1 -> Reg[RD] else 0 -> Reg[RD]

## Slide 5: ALU Register-Register Instruction formats

## Slide 6: ALU Register-Immediate Instructions
Encoding |  |  |  |  |  | OPC | Op1 | Op2 | Op3 | Operation
0 | 1 | 0 | 0 | 0 | 0 | ADDI | RS | RD | Imm | Reg[RS] + Immediate -> Reg[RD]
0 | 1 | 0 | 0 | 0 | 1 | SUBI | RS | RD | Imm | Reg[RS] - Immediate -> Reg[RD]
0 | 1 | 0 | 0 | 1 | 0 | ANDI | RS | RD | Imm | Reg[RS] & Immediate -> Reg[RD]
0 | 1 | 0 | 0 | 1 | 1 | ORI | RS | RD | Imm | Reg[RS] ¦ Immediate -> Reg[RD]
0 | 1 | 0 | 1 | 0 | 0 | XORI | RS | RD | Imm | Reg[RS] ^ Immediate -> Reg[RD]
0 | 1 | 0 | 1 | 0 | 1 | NANDI | RS | RD | Imm | ~(Reg[RS] & Immediate) -> Reg[RD]
0 | 1 | 0 | 1 | 1 | 0 | NORI | RS | RD | Imm | ~(Reg[RS] ¦ Immediate) -> Reg[RD]
0 | 1 | 0 | 1 | 1 | 1 | XNORI | RS | RD | Imm | ~(Reg[RS] ^ Immediate) -> Reg[RD]
0 | 1 | 1 | 0 | 0 | 0 | SLI | RS | RD | Imm | Reg[RS] << Immediate -> Reg[RD]
0 | 1 | 1 | 0 | 0 | 1 | SRI | RS | RD | Imm | Reg[RS] >> Immediate -> Reg[RD]
0 | 1 | 1 | 0 | 1 | 0 | SGEI | RS | RD | Imm | If Reg[RS] >= Immediate then 1 -> Reg[RD] else 0 -> Reg[RD]
0 | 1 | 1 | 0 | 1 | 1 | SGTI | RS | RD | Imm | If Reg[RS] > Immediate then 1 -> Reg[RD] else 0 -> Reg[RD]
0 | 1 | 1 | 1 | 0 | 0 | SLEI | RS | RD | Imm | If Reg[RS] <= Immediate then 1 -> Reg[RD] else 0 -> Reg[RD]
0 | 1 | 1 | 1 | 0 | 1 | SLTI | RS | RD | Imm | If Reg[RS] < Immediate then 1 -> Reg[RD] else 0 -> Reg[RD]
0 | 1 | 1 | 1 | 1 | 0 | SEQI | RS | RD | Imm | If Reg[RS] == Immediate then 1 -> Reg[RD] else 0 -> Reg[RD]
0 | 1 | 1 | 1 | 1 | 1 | SNEI | RS | RD | Imm | If Reg[RS] != Immediate then 1 -> Reg[RD] else 0 -> Reg[RD]

## Slide 7: ALU Register-Immediate Instruction formats

## Slide 8: Data Movement and Program Control Instructions
Encoding |  |  |  |  |  | OPC | Op1 | Op2 | Op3 | Operation
1 | 0 | 0 | 0 | 0 | 0 | LOAD | RS | RD | Imm | mem{Reg[RS] + Immediate} -> Reg[RD]
1 | 0 | 0 | 0 | 0 | 1 | STORE | RS | RD | Imm | Reg[RS] -> mem{Reg[RD] + Immediate}
1 | 0 | 0 | 0 | 1 | 0 | MOVE | RS | RD |  | Reg[RS] -> Reg[RD]
1 | 0 | 0 | 0 | 1 | 1 | MOVEI | Imm | RD |  | Immediate -> Reg[RD]
1 | 0 | 0 | 1 | 0 | 0 | BRA | RS | RSVal | Imm | If Reg[RS] == RSVal then PC + Immediate -> PC else PC + 2 -> PC
1 | 0 | 0 | 1 | 0 | 1 | JUMP | Imm |  |  | Immediate -> PC
1 | 0 | 0 | 1 | 1 | 0 | JREG | RS |  |  | Reg[RS] -> PC
1 | 0 | 0 | 1 | 1 | 1 | JAL | Imm |  |  | (PC + 2) -> Reg[R14], Immediate -> PC
1 | 0 | 1 | 0 | 0 | 0 | JALR | RS |  |  | (PC + 2) -> Reg[R14], Reg[RS] -> PC
1 | 0 | 1 | 0 | 0 | 1 | RET |  |  |  | Reg[R14] -> PC
1 | 0 | 1 | 0 | 1 | 0 | NOP |  |  |  | 

## Slide 9: Data Movement Instruction formats

## Slide 10: Program Control Instruction formats

## Slide 11: ALU Register-Register CPU Datapath

## Slide 12: SGE CPU Datapath

## Slide 13: SGT CPU Datapath

## Slide 14: ALU Register-Immediate CPU Datapath

## Slide 15: SGEI CPU Datapath

## Slide 16: Data Movement CPU Datapath

## Slide 17: Branch if Equal (BRA) CPU Datapath

## Slide 18: JUMP Instruction CPU Datapath

## Slide 19: JREG Instruction CPU Datapath